## Slide 1: A Tale of Two Cities: GPU Computing and Machine Learning
Dr. Xiaowen Chu
Department of Computer Science, Hong Kong Baptist University

## Slide 2: Outline
Some Stories of “Two Cities”
Evolution of CPUs/GPUs in the last decade
Roofline model: understand the GPU performance
GPU-accelerated machine learning tools
How does machine leaning affect/help GPU computing?

## Slide 3: Story I: Cat Detector
In ICML 2012 [1], Google and Stanford reported a deep neural network which builds features from unlabeled data.
  It can recognize “cat” by just watching YouTube.
But, 16,000 CPU cores x 3 days !!!
  Around HK$100,000 on Amazon EC2
One year later, the same task can be done by just 12 GPUs [2].
[Ref 1] Q. V. Le, et al. “Building High-level Features Using Large Scale Unsupervised Learning,” ICML 2012.
[Ref 2] A. Coates, et al. “Deep learning with COTS HPC systems,” ICML 2013.

## Slide 4: Story II:
Deep neural networks trained by supervised learning and reinforcement learning [3]
[Ref 3] D. Silver, et al. “Mastering the game of Go with deep neural networks and tree search,” Nature, Vol 529, Jan 2016.
Unsung heroes:
1,202 CPUs
+
176 GPUs

## Slide 5: Story III: Autonomous Cars
Deep learning techniques make autonomous cars into reality.
[Ref 4] M. Bojarski, et al. “End to End Learning for Self-Driving Cars,” Apr 2016, https://arxiv.org/abs/1604.07316 .
An End-to-end Solution [4]

## Slide 6: Story III (Cont.): Behind the End-to-End Solution
A CNN with 27mil links [4]
[Ref 4] M. Bojarski, et al. “End to End Learning for Self-Driving Cars,” Apr 2016, https://arxiv.org/abs/1604.07316 .
Trained on a workstation with four TITAN X GPUs
Operated on a self-driving car computer,
with dual Nvidia Tegra® X1 processors
(ARM CPU + GPU)

## Slide 7: 10 Years of Intel CPUs and Nvidia GPUs
Intel CPU: 15x of performance boost
Nvidia GPU: 20x of performance boost
Chart: 
| 2006 | 2008 | 2010 | 2012 | 2014 | 2016
GPU | 518 | 933 | 1331 | 5040 | 6840 | 10600
CPU | 42.56 | 63.84 | 85.12 | 185.6 | 547.2 | 633.6
GFlops
Always 10-15x over CPU
GeForce
8800 GTX
Tesla P100
Tesla M40
Tesla K40
Tesla M2090
GTX 280

## Slide 8: CPU/GPU Configurations
(a) Single GPU system
(b) Multi-GPU system
PCIe 3.0 (x16):
16GB/s
QPI:
25.6GB/s
CPU memory bandwidth:
70-80GB/s
GPU memory bandwidth:
240-720GB/s
(c) Data movement speed

## Slide 9: Example of GPU Architecture: Kepler [5]
15 Streaming Processors:
1.4TFlops
1536KB
L2 Cache
384-bit GDDR5 RAM:
288GB/s
32-bit SP ALU
64-bit DP ALU
[Ref 5] “NVIDIA’s Next Generation CUDATM Compute Architecture: Kepler TM GK110,” Nvidia Whitepaper, 2012.

## Slide 10: Myth of GPU Performance
A general question: what speedup can be achieved by GPUs (vs. CPU)?
The speedup depends on many factors:
  The nature of the application
    Amdahl's law / Sun-Ni’s law [6]
    Compute-bounded or bandwidth-bounded
  How do you design the parallel algorithm?
  How do you optimize the CPU code (multi-core, AVX, FMA)?
  How do you optimize the GPU code (more challenging)?
  etc.
Could be between 0.5x – 300x
[Ref 6] X.H. Sun and L. Ni, “Scalable Problems and Memory-Bounded Speedup,” JPDC, Vol. 19, p.27-37, Sept.1993.

## Slide 11: Challenge in GPU Computing
Big gap between processing capacity and memory access
  Computing is fast: each ALU can perform one or two operations per cycle. (1000 ALUs x 1GHz = 1TFlops)
  Long latency: hundreds of cycles to fetch data from DRAM
  Low memory bandwidth: 8.8TFlops vs. 320GB/s (GTX1080)
Access global memory
ALU
Access global memory
time
Perspective from a single thread
ALU
400 cycles
20 cycles

## Slide 12: Solution 1: Multithreading
Use multithreading to make the cores busy
  At least hundreds of thousands of threads
……
Access global memory
ALU
Access global memory
time
Perspective from multiple threads (for each multistage ALU pipeline)
ALU
ALU
ALU
ALU

## Slide 13: Solution 2: Memory Hierarchy [7]
[Ref 7] X. Mei and X.-W. Chu, “Dissecting GPU Memory Hierarchy through Microbenchmarking,” to appear in IEEE TPDS.
Regis ters
L1 cache
on/off?
Shared memory controlled by programmer
L2 cache
not controlled by programmer
Global memory

## Slide 14: Roofline Model [8]: Preliminaries
An insightful visual performance model that considers two major performance constraints:
  aggregated computational power of ALUs
  memory bandwidth
Operational intensity (OI): number of operations per byte of DRAM traffic. Assume single-precision operations,
  Dot product: z = xy, OI = 1/4
  Dense Matrix-vector multiply: y = Ax, OI = 1/2
  Sparse Matrix-vector multiply: y = Ax, OI = 1/8 to 1/4
  Dense Matrix-matrix multiply: Cnxn = AnxnBnxn, OI ϵ [1/4, n/6]
[Ref 8] S. Williams, et al. “Roofline: An Insightful Visual Performance Model for Multicore Architectures,” Communications of the ACM, Vol. 52, No. 4, Apr 2009.

## Slide 15: A Simple Roofline Model: PERF = MIN(FP_PERF, DRAM_BW x OI)
Operational Intensity (Flops/Byte)
GFlops
Peak DP performance
Peak Stream Bandwidth
75
Intel Xeon E5345
FP_PERF = 75GFlops, DRAM_BW = 10GB/s
Performance
1
1/16
1/8
8
1/4
1/2
1
2
4
Memory-bounded
Compute-bounded
16
32

## Slide 16: An Example of GPU Roofline Model
Operational Intensity (Flops/Byte)
Peak SP performance
Peak GM Bandwidth
4600
Performance (GFlops)
1
1/16
1/8
8
1/4
1/2
1
2
4
10
NVIDIA GTX980
FP_PERF = 4600GFlops, SM_BW = 2000GB/s, GM_BW = 156GB/s
16
32
140
Peak SM Bandwidth
64
Dense matrix multiply
Reduction, sparse operation, etc
FFT

## Slide 17: Machine Learning Tools that Support GPUs
GPUMiner
2008 [9]
BIDMach
2013
Caffe
2014
TensorFlow
2015
CNTK
2015
DSSTNE
2016
[Ref 9] W. Fang, et al. “Parallel Data Mining on Graphics Processors,” Technical Report HKUST CS0807, Oct 2008.

## Slide 18: General ML: BIDMach [10]
A framework for developing general ML algorithms with GPUs
Implemented algorithms:
  Logistic and Linear Regression, Support Vector Classification, Factorization Machines, Sparse Factor Analysis, Topic Models: Latent Dirichlet Allocation, Non-negative Matrix Factorization, Simple Deep Neural Networks, K-Means, Random Forests …
Benchmarking results (2015): https://github.com/BIDData/BIDMach/wiki/Benchmarks
[Ref 10] H. Zhao, et al. “BIDMach: A Very Fast and Scalable ML Toolkit for Big Data,” under submission.
One GPU can beat large CPU cluster in many cases!

## Slide 19: Arms Race in Deep Neural Networks: Caffe, CNTK, TensorFlow, DSSTNE
 | Caffe | CNTK | TensorFlow | DSSTNE
Provider | UC Berkeley | Microsoft | Google | Amazon
Release date | Jun 2014 | Dec 2015 | Nov 2015 | Jan 2016
APIs | C/C++, Python, Matlab | C++; Python, C# (in plan) | C++, Python | No
Multi-GPU support | Yes | Yes | Yes | Yes
GPU cluster support | CaffeOnSpark (by Yahoo) | Yes | Yes | Yes
CUDA library | cuDNN(v4, v5) | cuDNN(v4) | cuDNN(v4,v5) | cuBLAS
OS support | Linux, MacOS, Windows | Linux, MacOS, Windows | Linux | Linux/Docker/AWS

## Slide 20: Some Benchmarking Results
Chart: 
| TensorFlow | Caffe | CNTK
GPU | 58.7719 | 61.8081 | 46.5278
CPU | 1.5172 | 1.2594 | 1
ImageNet (AlexNet)
Speedup
Nvidia GTX980
Intel quad-core
i7-3770
Speedup
MNIST (LeNet)
Chart: 
| TensorFlow | Caffe | CNTK
GPU | 14.1698 | 30.0815 | 19.7632
CPU | 1 | 1.0925 | 1.3143

## Slide 21: Some Benchmarking Results (Cont.)
DSSTNE is designed for sparse data
  Deep Scalable Sparse Tensor Network Engine
Experiments:
  Dataset: MovieLens 20M view
    20 million ratings and 465,000 tag applications applied to 27,000 movies by 138,000 users
  Network: 5-layer AutoEncoder
Our benchmarking results:
  TensorFlow on GPU is 20x faster than on CPU
  But, DSSTNE is 15x faster than TensorFlow on GPU!

## Slide 22: How does ML Affect GPU Computing?
The success of ML makes a huge impact on the design of new GPU architectures
Nvidia’s latest GPU, Tesla P100, is designed to fit deep learning [11]
  16-bit half-precision (HP) floating point operations
    Users can choose 21.2TFlops in HP or10.6TFlops in SP
  3D stacked memory (HBM2)
    Size = 16GB, bandwidth = 720GB/s
  NVlink: to connect multiple GPUs
    160GB/s bidirectional link between GPUs
[Ref 11] “NVIDIA Tesla P100,” Nvidia Whitepaper, 2016.

## Slide 23: How does ML Help GPU Computing?
TITAN (with18,688 GPUs) consumes 8.2 MW of power, i.e., 70mil kiloWatt-hour per year.
How to reduce the power consumption of GPU cluster?
  Task mapping, scheduling, DVFS, etc.
Two major ingredients
  How to predict the running time of a given task?
  How to predict the power consumption of a given task?
N: number of tasks
Pi: average power of task i
ti: running time of task i
Machine learning plays a major role in these prediction problems.

## Slide 24: Summary
For ML practitioners
  Understand the nature of your ML algorithm
  Choose appropriate hardware platform
  Choose appropriate software that fits your hardware & ML algorithm
  Learn cuBLAS, cuDNN, cuSPARSE, cuFFT, etc.
For GPU community
  Understand the need of ML community
  Improve the scalability
  Reduce communication overhead
  Better sparse operations
  More energy efficient

## Slide 25
By Yan Qing Chu
16/6/2016